## Slide 1: DES: Instrument Cluster
Team 03
Kijin Baek
Saicharan Sathyam

## Slide 2: Presentation Agenda
Overview of the Instrument Cluster system and its key features
Detailed hardware requirements and system architecture
Sensor node operations and data communication flow
Remote control and cross compilation techniques
Qt5/QML GUI implementation and performance optimizations
Summary of data communication and system integration

## Slide 3
Key Features
Real-time Speed Display
Speed monitoring in cm/s with Kalman Filtering for smooth readings
Battery Display
Shows battery percentage with visual indicator
Gear Display
Shows current gear (P/R/N/D)
Turn Signal Indicators
Left/right turn signals with blinking animations
Cross Compilation
Runs on development machine and cross-compiles for Raspberry Pi 4

## Slide 4
Hardware Requirements
Raspberrry Pi
CAN_BUS HAT
7.9inch Display

## Slide 5
Hardware Requirements
Arduino Uno
CAN_BUS Sheild
Speed Sensor (LM 393)

## Slide 6
Hardware Requirements
PiRacer Standard Kit
Joystick

## Slide 7
System Overview
Arduino (sensors)
CAN Bus
D-Bus Service
Remote Control
QT5/QML GUI

## Slide 8
Arduino Sensor Node
Real-time Processing
Setup CAN Controller
Configure MCP2515 for communication
Configure Speed Sensor
Set up encoder interrupt handling
Calculate Speed
Process encoder pulses
Send Data
Transmit speed via CAN (ID: 0x100) every 50ms

## Slide 9
CAN Thread
Receive speed, apply Kalman Filter
Battery Thread
Poll INA219 sensor every second
D-BUS Methods
Handle Gear and Turn Signals
Signal Emissions
Emits updates to GUI
D-Bus Service

## Slide 10
2-State Kalman Filter Execution
State Prediction
(Velocity, Acceleration)
Sensor Measurement
(Arduino CAN Message)
Innovation Calculation (Prediction Error)
Kalman Gain Computation
(K = 0-1)
State Update
(Corrected speed based on K and Innovation)
Covariance Update
(Confidence adjustment)
Output Generation
(Filtered output to DBus)

## Slide 11
Remote Controller
Initialize Gamepad and PiRacer
Connect to D-Bus service
Read D-Pad Input
Read Turn Signal Buttons
Apply Gear Based Logic
Set Steering and Throttle
Send Gear Commands
Send Turn Signal Commands
Read Gamepad Input

## Slide 12
Cross Compilation
Host
x86_64 Ubuntu Development Machine
Target
ARM64 Raspberry Pi4 (aarch64)
Compilation Strategy
Stage 1: Use host (x86_64) Qt tools to generate C++ code from your Q_OBJECT classes
Stage 2: Cross-compile the generated code using ARM64 toolchain
Stage 3: Link with target libraries from the sysroot

## Slide 13
Qt5/QML GUI Implementation
Architecture and Data Flow :
[CAN Bus] → [Python Aggregator] → [D-Bus Service]
[C++ Bridge: PiRacerBridge]
[QML GUI: main.qml]
Key Design Pattern :
D-Bus signals → C++ slots → Qt properties → QML bindings
Initial value fetch via D-Bus methods prevents empty UI on startup
Change detection prevents redundant UI update

## Slide 14
Qt5/QML GUI Implementation
Performance Optimizations :
GPU-friendly animations with easing curves
Property binding efficiency - updates only on actual value changes
60 FPS rendering with smooth transitions (180-400ms timing)

## Slide 15
Data communication flow

## Slide 16
Result